## Slide 1
DDCA PROJECT
DESIGN AND
SIMULATION OF
DIGITAL DATA
TRANSMISSION
ERROR DETECTION
SYSTEM
A digital communication link that detects corrupted data using redundant check bits and receiver-side validation.
EDITABLE STUDENT DETAILS
[Student Name • Roll No.]
[Guide Name]
[Department • College]
Academic Year 2026–27
DATA
ENCODE
CHANNEL
CHECK
01 10 111 001

## Slide 2
01 • INTRODUCTION
Why error detection matters in digital transmission
Bits can be flipped by noise, interference or timing issues. The receiver needs a fast, deterministic way to decide: “accept or reject?”
THE CORE IDEA
Add
structured redundancy
→ send
→ verify
→ flag errors
TRANSMITTER
RECEIVER
DECISION
DATA IS FRAGILE
A single altered bit can change a command, character, address or measurement.
REDUNDANCY HELPS
Parity, checksums and CRCs append information that reveals inconsistencies.
SIMULATION MAKES IT VISIBLE
A Logisim model turns the algorithm into gates, wires, registers and testable outputs.
DETECT
DESIGN TARGET
LOGISIM
IMPLEMENTATION
VALID / ERROR
OUTPUT

## Slide 3
02 • PROBLEM STATEMENT
The problem: transmission can silently corrupt data
The system should make corruption observable without needing to “know” the original message at the receiver.
UNPROTECTED LINK
1
0
1
1
0
1
0
0
TX
NOISE
/ INTERFERENCE
1 0 1 1 0 0 0 0
The receiver may accept corrupted data if there is no integrity check.
LIMITATION
No confidence signal • No explicit error flag • Difficult to demonstrate fault behavior
01
Detect corruption
Know whether received bits violate the designed check rule.
02
Localize the decision
Produce a clean VALID / ERROR output for the receiver.
03
Prove it in simulation
Inject an error and show the logic responds predictably.

## Slide 4
03 • OBJECTIVES
What the project is designed to achieve
Turn a textbook error-detection method into a visible, testable digital system in Logisim.
DESIGN
Build a transmitter → channel → receiver chain with a defined redundancy rule.
SYSTEM DESIGN
DETECT
Identify whether the received word is consistent with the transmitted format.
SYSTEM DESIGN
SIMULATE
Implement the logic using gates, registers, multiplexers and indicators in Logisim.
SIMULATION DEMONSTRATION
DEMONSTRATE
Inject controlled bit errors and observe the resulting ERROR flag.
SIMULATION DEMONSTRATION
Success condition → a controlled error produces a deterministic, visible ERROR indication at the receiver.

## Slide 5
04 • LITERATURE SURVEY
Existing error-detection approaches — and where this project fits
The project emphasizes explainability: the algorithm should be easy to trace from bits → logic → receiver decision.
METHOD
CORE IDEA
STRENGTH
LIMITATION
Parity
Add 1 bit so the number of 1s follows a rule.
Very simple; low hardware cost.
Limited detection capability.
Checksum
Aggregate data into a compact check value.
Good for blocks of data.
More arithmetic hardware.
CRC
Polynomial-based redundancy; receiver checks the remainder.
Strong detection for structured bit errors.
Needs divider / LFSR-style logic.
This project
CRC-style receiver decision in Logisim.
Transparent, visual, testable.
Simulation is not a full physical link.
Design choice → use a small CRC-style check because it maps cleanly to XOR + shift-register logic and produces an intuitive “remainder = 0” receiver test.

## Slide 6
05 • PROPOSED SYSTEM
Proposed architecture: transmit, perturb, verify
The design separates the communication path from the integrity decision so each block can be tested independently.
DATA
SOURCE
Plain bit stream
ENCODER
Generate check bits
CHANNEL
Optional bit flip
CHECKER
Recompute / compare
OUTPUT
VALID / ERROR
ERROR
INJECT
flip 1 bit
XOR NETWORK
Generate/check parity relation
SHIFT REGISTER
Hold / shift incoming bits
COMPARATOR
Convert mismatch to flag
LED / PROBE
Make result visible in Logisim

## Slide 7
06 • METHODOLOGY
Implementation workflow: from algorithm to gates
A compact CRC-style example is used for the demonstration; the exact polynomial/data width can be changed in the circuit.
1
CHOOSE RULE
Select a generator polynomial / redundancy rule.
2
APPEND CHECK
Form the protected codeword from payload + check bits.
3
TRANSMIT
Send the codeword through the simulated channel.
4
RECHECK
Run the receiver check; valid codeword → zero remainder.
5
FLAG
Non-zero remainder → ERROR indicator.
REPRESENTATIVE CRC STEP
Generator: x³ + x + 1
Binary form: 1011
1
1
1
1
0
0
0
⊕
shift → XOR → shift → repeat
Receiver rule
remainder = 000 → VALID
remainder ≠ 000 → ERROR
LOGISIM PROBES
data • check bits • error flag

## Slide 8
07 • CIRCUIT IMPLEMENTATION
Logisim implementation: modular, testable, easy to demo
The circuit can be organized as reusable subcircuits so the top-level schematic stays readable during evaluation.
TOP-LEVEL CIRCUIT
INPUT
REGISTER
D[7:0]
CRC
ENCODER
XOR + SHIFT
CHANNEL
MUX
ERR BIT
CRC
CHECKER
REMAINDER
LED
VALID / ERROR
SUBCIRCUITS
A
Encoder
generates redundant bits
B
Error Injector
flips a selected bit
C
Checker
recomputes remainder
D
Decision
lights VALID / ERROR
Demo tip
Keep one probe on the remainder; it makes the “why” behind ERROR immediately visible.

## Slide 9
08 • RESULTS & DISCUSSION
Test matrix: show the detector doing its job
Use these cases as the minimum demonstration set in Logisim; replace the placeholders with your actual screenshots/observed waveforms.
#
TEST CASE
EXPECTED RECEIVED
FLAG
INTERPRETATION
1
No error
Matches transmitted codeword
VALID
Normal transmission
2
Flip 1 payload bit
Codeword becomes inconsistent
ERROR
Single-bit fault detected
3
Flip 1 check bit
Remainder becomes non-zero
ERROR
Redundancy bit corruption detected
4
Error injection OFF→ON
Flag changes only when fault enabled
VALID → ERROR
Demonstrates control logic
LOGISIM RESULT AREA
[ INSERT YOUR .CIRC CIRCUIT SCREENSHOT HERE ]
Recommended screenshot: top-level circuit + visible probes + ERROR LED
PASS
CASE 01
FLAG
CASE 02
FLAG
CASE 03

## Slide 10
09 • CONCLUSION
From algorithm to observable hardware behavior
The project connects a digital communication concept to a concrete, demonstrable circuit.
“The receiver does not need to trust the channel — it only needs to verify the rule.”
DESIGNED
A modular transmitter–channel–receiver chain was defined.
IMPLEMENTED
CRC-style checking logic was mapped into Logisim components.
VALIDATED
Controlled bit flips produce a visible ERROR decision.
NEXT ITERATION
Extend to wider payloads, stronger CRC polynomials, burst-error experiments, and a cleaner waveform/probe view.

## Slide 11
10 • SUBMISSION READY
GitHub project structure & evaluation checklist
Keep the repository visibly aligned with what you present in the PPT.
REPOSITORY
DDCA-Error-Detection-System/
├──
README.md
project overview + how to run
├──
project.pptx
presentation submitted
├──
error_detection.circ
Logisim circuit
├──
/screenshots/
circuit + result captures
└──
/docs/
notes / report / references
COMMIT HISTORY
Use meaningful commits: design → encoder → checker → test → documentation
FINAL CHECK
✓
PPT = 8–12 slides
✓
.circ file opens and shows actual project progress
✓
Implementation/screenshots match the PPT claims
✓
README explains the project + simulation steps
✓
All project work is committed and pushed
✓
Repository history reflects incremental work
REFERENCES
Digital Communications • Error Detection / CRC fundamentals • Logisim documentation